## Slide 1: Less Waste, Better Baltimore
Rethinking our waste management future
Update on the LWBB Plan
20 November 2019
1

## Slide 2: Outline
Review scope and progress on LWBB Plan
Review of recycling and diversion options
  Basis and methodology
  Options analysis
Summary of findings
2

## Slide 3: LWBB Project Scope
Master planning effort through 2040+
Identify programs that could be implemented by DPW to:
Reduce the amount of waste generated
Maximize materials diversion, reuse, and recycling
Identify the best options for disposing of what’s left
3

## Slide 4: Process for Plan Development and Execution
Winter/Summer Waste Sorts
4x Community Meetings
Online Survey/Email Feedback
Review of Baltimore’s Existing System
Benchmarking Against Other Cities
Review Options for Improving Waste Diversion
Handling What's Left
Assess Potential Impact on Waste Diversion Rate
4
Task 5
Task 7
Tasks 0 - 4

## Slide 5: Options for Increasing Waste Diversion
How do we go about analyzing the City’s waste flows in order to understand how to reduce waste generation and divert more material from disposal?
 Understand waste flows and materials
 Look at what options are available and would be supported by residents and other stakeholders
 Objectively assess different options in terms of expected performance
5

## Slide 6: Options for Increasing Waste Diversion
How do we go about analyzing the City’s waste flows in order to understand how to reduce waste generation and divert more material from disposal?
 Understand waste flows and materials
 Look at what options are available and would be supported by residents and other stakeholders
 Objectively assess different options in terms of expected performance
6

## Slide 7: Waste Flows in Baltimore City
7
Current disposal flows that are the focus of this analysis

## Slide 8: Estimated Quantities of Materials (2017-19 data)
Category | Residential Waste (tons) | Commercial Waste (tons) | Total (tons)
Total Disposal | 319,500 | 505,100 | 824,600
Food and Other Compostables | 101,700 | 61,500 | 163,200
Cardboard | 24,600 | 32,400 | 57,000
“Easy-to-Recycle” Materials | 34,000 | 28,600 | 62,600
“Hard-to-Recycle” Materials | 73,900 | 47,400 | 121,300
Lumber | 2,400 | 22,000 | 24,400
Other Mixed C&D Waste | 3,100 | 261,200 | 264,300
Bulky Waste, Mattresses, Carpets | 2,800 | 2,900 | 5,700
Unclassified (Disposal) | 77,000 | 49,300 | 126,300

## Slide 9: Options for Increasing Waste Diversion
How do we go about analyzing the City’s waste flows in order to understand how to reduce waste generation and divert more material from disposal?
 Understand waste flows and materials
 Look at what options are available and would be supported by residents and other stakeholders
 Objectively assess different options in terms of expected performance
9

## Slide 10: Stakeholders Invited to Participate
Anchor Institutions
Businesses
Community organizers/leaders
Economic development partnerships
Elected officials
Environmental protection groups
Residents
Other City agencies/partnerships
Port Authority
Schools
Students
Waste management companies
10

## Slide 11: Public Input
11

## Slide 12: Benchmarking – Learning from Other Cities
12
Portland OR
Austin TX
Charleston SC
Charlotte NC
Boston MA

## Slide 13: Options for Increasing Waste Diversion
How do we go about analyzing the City’s waste flows in order to understand how to reduce waste generation and divert more material from disposal?
 Understand waste flows and materials
 Look at what options are available and would be supported by residents and other stakeholders
 Objectively assess different options in terms of expected performance
13

## Slide 14: Baltimore City’s Strategic Plans
Zero waste goal of 90% diversion
Increase recycling
Reduce litter
Legislative and policy changes
Waste-to-Wealth Initiative:
Food waste
C&D waste
Wood
Goals for 2040
50% food waste reduction
80-90% diversion of food waste from disposal to composting and digestion
25% reduction in greenhouse gas emissions by 2020 and 30% reduction by 2025
14

## Slide 15: Methodology for Assessment
Challenges to Implementation:
Permits
Infrastructure and Land Required
Training
Costs:
Capital
Operation and Maintenance
Labor
Waste Diversion Potential:
Total tonnage
Materials
Interaction with Other Options
Benefits:
Social/Environmental
Greenhouse Gas Emissions
Job Creation
Revenue/Cost Offsets
Timeline:
Short – Medium – Long Term
Time Lag before Seeing Benefits
Experience:
DPW’s Experience
Local Private Sector Experience
Other Jurisdictions
15

## Slide 16: Analysis of Waste Recycling/Diversion Options Task 5 of LWBB Plan
Draft Report Submitted to DPW on 30 Oct.
  Chapters 1 and 2 – Basis for Evaluation
  Chapter 3 – Food Waste and Organics
  Chapter 4 – “Traditional” Recyclables
  Chapter 5 – Construction and Demolition Waste
  Chapter 6 – “Non-Traditional” Recyclables
  Chapter 7 – Multi-Purpose Facilities
  Chapter 8 – “Soft” Infrastructure
  Chapter 9 – Operational and Administrative Improvements
  Chapter 10 – Summary of Findings

## Slide 17: Ch. 2 – Assessment of Overall Divertability DRAFT FINDINGS ONLY
17
Total waste generated
1,641,800 tons
Recycled
738,500 tons
Composted
78,700 tons
Disposal
824,600 tons
~50%
Baltimore Sustainability Plan (BSP) states 90% diversion goal
Additional diversion required
= 40% of total (656,700 tons)
BSP Goal for LWBB Plan
Potential Diversion
43% of total (698,300 tons)
Disposal
Based on
2017 data

## Slide 18: Ch. 10 – Maximum Diversion Potential (MDP) DRAFT FINDINGS ONLY
18
Chapter | Description | Universal Application | Food Waste Strategy |  | C&D Waste Strategy | 
 |  |  | A | B | A | B
3.1 | Food Waste Reduction |  | - | 72,400 |  | 
3.2 | Residential Organics Composting |  | 81,800 | 42,800 |  | 
3.3 | Commercial Organics Composting |  | 59,200 | 35,500 |  | 
4 | Traditional Recyclables | 153,500 |  |  |  | 
5.1 | C&D Reuse |  |  |  | - | 28,400
5.2 | C&D Diversion |  |  |  | 216,900 | 200,100
6.1 | Bulk Waste | 4,000 |  |  |  | 
7.1 | Expand Residents’ Drop-offs | 16,100 |  |  |  | 
10 | Subtotal | 173,600 | 141,000 | 150,700 | 216,900 | 228.5k
Available Diversion = Universal + A/B from Food Waste Strategy + A/B from C&D Waste Strategy
Maximum Diversion Potential (MDP) Highlighted in Red = 173.6k + 150.7k + 228.5k = 552.8k tons
Achieving MDP would increase overall waste diversion to 83% (552.8k + 738.5k + 78.7k / 1641.8k = 0.83)

## Slide 19: Ch. 10 – Direct Cost and Benefits (for MDP) DRAFT FINDINGS ONLY
19
Chapter | Description | CAPEX $/ton |  | OPEXA $/ton |  | Job Creation Potential |  | GHG Reduction MTCO2E
 |  | DPW | Total | DPW | Total | DPW | Others | 
3.1 | Food Waste Reduction | -- | $687 | $65 | $3,415 | 3 | not calc. | 305,000
3.2 | Residential Organics | $166 | $415 | $146 | $230 | -- | 40C | 4,500
3.3 | Commercial Organics | -- | $331 | $8 | $197 | 3 | 70C | 800
4 | Traditional Recyclables | $128 | $236 | $120 | $184 | 4 | 120C | 349,700
5.1 | C&D Reuse | -- | -- | $5 | $5B | 3 | --B | 25,000
5.2 | C&D Diversion | -- | $103 | -- | $91B | -- | 30B,C | 32,700
6.1 | Bulk Waste | -- | -- | $12 | $12B | 6 | 6B,C | 11,400
7.1 | Resid. Drop-offs | $12 | $12 | $22 | $22 | 6 | 6C | 25,800
10 | All | $262 (weighted avg.) |  | $563 (weighted avg.) |  | 25 | ~270 | 754,900
A: excl. revenues from sale of recovered materials, tip fees; B: excl. secondary job creation; C: excl. job losses at disposal facilities

## Slide 20: Ch. 10 – Timeline and Phasing (for MDP) DRAFT FINDINGS ONLY
20
Chapter | Diversion Option | Timeframe (years) | Diversion Potential (tons)
3.1 | FW Red. | 20 | 0k or 72.4k
3.2 | Resid. Org. | 20 | 81.8k or 42.8k
3.3 | Comm. Org. | 20 | 59.2k or 35.5k
4.2 | Trad. Recyc. | 10 | 153.5k
5.1 | C&D Reuse | 10 | 0k or 28.4k
5.2 | C&D Div. | 20 | 216.9k or 200.2k
6.1 | Bulk Waste | 10 | 4k
7.1 | Res. Dropoff | 5 | 16.1k
Timeframe for achieving Max. Diversion Potential (MDP) for each Option
Assumed S-Curve Uptake Rate for each Option
Example:
How much additional diversion of Trad. Recyclables is expected under the MDP in 2032 if the program starts in 2025?
 10-year implementation timeframe. S-Curve: 0% = 2025, 100% = 2035. 2032 = 7 years in. 7YR/10YR = 70%
 70% of timeframe = 85% of diversion potential. 85% x 153.5k = 130.5k tons.

## Slide 21: Ch. 10 – Range of Diversion Outcomes DRAFT FINDINGS ONLY
21
Range of Potential Diversion Rates
(depending on when each option starts and how successful it is)

## Slide 22: Ch. 10 – What’s Left for Disposal under MDP DRAFT FINDINGS ONLY
22
Historical and Projected Waste Generation
(growth projection = 0.7% per year)
What’s Left for Disposal
(assuming the City achieves MDP by 2040)
(assuming 0.7% annual growth in all waste streams)
2017

## Slide 23: Ch. 10 – Range of Disposal Outcomes (Citywide) DRAFT FINDINGS ONLY
MDP | 2020 | 2025 | 2030 | 2035 | 2040
0% | 463,700 | 479,700 | 496,200 | 513,200 | 530,800
20% | 463,200 | 462,100 | 453,600 | 465,900 | 483,100
40% | 462,600 | 444,600 | 410,700 | 413,900 | 428,600
60% | 462,100 | 427,200 | 367,400 | 357,000 | 367,300
80% | 461,600 | 409,900 | 323,700 | 295,200 | 299,200
100% | 461,000 | 392,700 | 279,500 | 228,700 | 224,400
MDP | 2020 | 2025 | 2030 | 2035 | 2040
0% | 249,800 | 258,400 | 267,200 | 276,400 | 285,900
20% | 249,400 | 251,000 | 241,200 | 225,000 | 226,000
40% | 249,000 | 243,500 | 215,500 | 178,400 | 172,700
60% | 248,500 | 236,000 | 190,300 | 136,600 | 126,300
80% | 248,100 | 228,300 | 165,500 | 99,600 | 86,600
100% | 247,700 | 220,500 | 141,000 | 67,500 | 53,700
Expected C&D Disposal Tonnages under Various Diversion Rates as a Percentage of the MDP
(0% represents Status Quo)
Expected MSW Disposal Tonnages under Various Diversion Rates as a Percentage of the MDP
(0% represents Status Quo)
Looking forward to Task 7: What does this mean for the City’s disposal needs?

## Slide 24: Ch. 10 – Range of Outcomes for DPW DRAFT FINDINGS ONLY
MDP | 2020 | 2025 | 2030 | 2035 | 2040
0% | 271,700 | 281,000 | 290,700 | 300,700 | 311,000
20% | 271,300 | 270,300 | 264,200 | 266,600 | 275,400
40% | 271,000 | 259,600 | 237,700 | 232,400 | 239,800
60% | 270,600 | 248,800 | 211,300 | 198,300 | 204,200
80% | 270,300 | 238,100 | 184,800 | 164,100 | 168,500
100% | 269,900 | 227,300 | 158,300 | 130,000 | 132,900
TRASH FOR DISPOSAL
Expected DPW curbside trash collection (tons) under Various Diversion Rates as a Percentage of the MDP
(0% represents Status Quo)
What does this mean for DPW’s collection and disposal needs?
MDP | 2020 | 2025 | 2030 | 2035 | 2040
0% | 31,600 | 32,700 | 33,800 | 34,900 | 36,100
20% | 31,900 | 43,400 | 60,300 | 69,100 | 71,800
40% | 32,300 | 54,100 | 86,700 | 103,200 | 107,400
60% | 32,600 | 64,900 | 113,200 | 137,300 | 143,000
80% | 33,000 | 75,600 | 139,700 | 171,500 | 178,600
100% | 33,400 | 86,400 | 166,200 | 205,600 | 214,300
RECYCLING + ORGANICS
Expected DPW curbside collection (tons) under Various Diversion Rates as a Percentage of the MDP
(0% represents Status Quo)

## Slide 25: Thank You
Less Waste, Better Baltimore
Rethinking our waste management future
publicworks.baltimorecity.gov/lesswaste
25